Drive Cycle Generation Tutorial

THE SCRIPT ‘DC’ EXECUTES ALL OF THE FOLLOWING SCRIPTS AND FUNCTIONS.
Matlab command: dc

Events Extraction
First, the script ‘mode’ extracts the events -accelerations, decelerations, cruises and idles- from the standard drive cycles or any other dataset.
!! The dataset must be in meter per second ‘m/s’!!
Matlab command: mode

Targets Creation
The function ‘extract_targets’ extracts the information from the Excel file named ‘file’ and creates the structure ‘targets’ with fields ‘distance’, ‘time’, and ‘mean speed’. In the current program, the file of trips is named ‘x12dc’.
Matlab command: targets = extract_targets(‘x12dc’)

Inputs Addition
The program needs some additional inputs: ratio of the distance on highway over the distance on city roads, and the highway mean speed.
The script ‘hwy_info’ adds these inputs to the structure ‘targets’ by creating the fields ‘ratio_hwy’ and hwy_speed’.
Matlab command: hwy_info

Inputs Checking
The function ‘do_inputs_make_sense’ allows the user to check if the mean speeds and times on highway and city roads are realistic. The matrix ‘inputs_check’ stores all these information.
To have realistic drive cycles, the time on highway should be long enough if the mean speed is above 50 mph or the mean speed should be lower than 30 mph if the time on highway is short (about 10 min).
Matlab command: inputs_check = do_inputs_make_sense(targets)

Drive Cycles Generation
The function ‘create_dc’ generates the desired number of drive cycles for every target trip.
Matlab command: drive_cycles = create_dc(modes,targets)
‘create_dc’ calls the function ‘cherry’ which uses the functions ‘dc_city’ to create the city portions and ‘dc_hwy’ to create the highway portion.